marvent Lp

CONNECTOR CAP FIXING INSTRUCTIONS

# Text boxes

1	Without using excess force, gently bend the sides of the PVC connector cap towards you

2	Apply a narrow bead of clear silicone along the aluminium glazing connector

3	Run finger along glazing connector to remove excess silicone

4&5	Apply a narrow bead of silicone along each side of the PVC connector cap

6	As above, run finger along to remove excess silicone

7	Put PVC connector cap in place above the aluminium glazing connector

8	Press firmly until connector cap engages into the channels of the aluminium glazing connector

9&10	Still pressing down firmly, move your had and thumb slowly along the remainder of the PVC connector cap

11	With a cloth, wipe off excess silicone along the gasket edge of the PVC connector cap

3

4

2

1

6

7

8

5

10

12&13

Fixing complete

9

11

12

13